### 39' Beneteau Oceanis 393  18 July 2006

SPECS

- Year: 2001

- Current Price: £ 60,000 Tax Not Paid   (US$ 110,706)  Standing Offer: $106,000

- Located In Orhaniye, Turkey

- Hull Material: Fiberglass

- Engine/Fuel Type: Single Diesel

- YW# xxx

- Designer: Berret/Racoupeau

- LOA: 11.95 Beam: 3.96/12 ft 11 in	Displacement: 7,200 kg

- Engine(s): 56hp Yanmar 4JH3E diesel engine

- Fuel: 150 litres Water: 500 litres Holding: x 2

Accommodation Accommodation sleeps 8 in 3 double cabins plus saloon. Fwd master suite features pulman style berth & seperate seating area. Saloon table converts to a double berth with saloon infill cushions. Dark blue velour upholstery in good condition. Cherry wood and wood-faced ply, synthetic laminate flooring & Formica on hard wear areas. Fans in galley, cabins & saloon. Max headroom: 2.10m

Galley & Heads Lateral galley equipped with Eno two-burner propane gas cooker with oven & grill, Frigoboat engine-driven refrigeration system with large top opening fridge and double stainless steel sink. Two heads equipped with Jabsco toilets, holding tanks, hand basins, showers & mirrors. Fowd head is en suite from master cabin. Hot & cold pressurised water in heads and galley. Cold water transom shower. Foot pump in galley acts as fridge drain.

Mechanical Systems 56hp Yanmar 4JH3E, 4 cylinder diesel engine (2001). Engine No. E23669 Last major service April 2006. Weekly checks between charters during season. Engine hours: 2483 at 22/7/06 Shaft drive to fixed 3-bladed propeller.

Electrical Systems 1 x 80Ah engine start battery. 2 x 80Ah domestic batteries. 12v on board systems. 220v shore power connection with cable. 80A alternator & battery charging relay. 12v sockets at chart table and in saloon. 2 pin 220v sockets at chart table, in cabins and in galley & saloon.

Spars & Sails Mast head sloop rig with rigid vang. Z Spar anodised aluminium mast & boom. Profurl genoa furling drum & foil. Stainless steel wire rope 1X19 Neil Slab reefing mainsail with lazy jack system & green sail bag . Elvstrorm Roller furling genoa with green UV protection strip. Braided rope running rigging led to cockpit.

Deck Equipment 2 x Lewmar 48 self-tailing two speed genoa winches on cockpit coming. 2 x Lewmar 30 self-tailing two speed halyard winches on coach roof. Adjustable genoa tracks on side decks. Deck organisers & adjustable main sheet traveller on coach roof.

Navigation Equipment Navico RT1200 VHF radio with cockpit speaker. Raymarine ST60 Tridata speed/depth/log unit. Raymarine ST6000+ autopilot. Raymarine ST60 anemometer. Garmin G126 GPS unit at chart table Nawman chart plotter mounted at chart platter Plastimo steering compass mounted on binnacle. Plastimo clock & barometer at chart table. Navigation, mooring & steaming lights.

Safety Equipment Zodiac 8 man life raft (last inspected 2/2006) 4 x fire exinguishers (last inspected 1/2006) Fire blanket. 8 x life jackets & safety harnesses. Flare pack. Emergency tiller. Manual bilge pump in cockpit. Electric bilge pump with switch at fuse panel. Horseshoe lifebuoy. Floating distress light. Guard wires, pushpit & pulpit.

Inventory JVC radio/CD player with interior & external speakers. Outboard engine storage bracket mounted on pushpit (no outboard). Swim ladder & cold water shower on transom. Bimini awning with folding stainless steel support frame. Boat hook. 4 x warps. 6 x fenders. Cutlery, crockery & utensils for 8 people.

Ground Tackle Delta bow anchor with approx 40m chain & 5m warp. Brittany kedge anchor with approx 5m chain & 10m warp. Lofrans Tigres electric anchor windlass with 10mm gypsy. Operates only with engine running with controls from fwd heads.

History & Construction This yacht has been professionally maintained by Yacht Charters from her delivery from the factory until now. During this charter history, a full systems check is done between each and every charter and all necessary repairs are made. This means that the average charter yacht in our fleet spend between 20 - 30 days per year on our maintenance docks where our trained mechanics, technicians, and cleaners make sure that our yachts are in the best of condition. This boat has chartered in Corsica, Croatia and Turkey. It will operate as part of the Dorian 1 week flotilla from our Orhaniye base during the 2006 season and will be available for sale from 15th November 2006. Hull no: FR-BEYA Flag: French Port of Registry: St Raphael Registration No: xx Build & Model year: 2001 First charter: 7/04/2001 GRP hull & deck construction with teak inlay on cockpit seating and transom. Spade rudder. Fin keel with bulb. Single steering position. Two coats of antifoul treatment on commissioning, with annual maintenance thereafter.